Messaging Reply To pattern

The Reply To pattern is a way to implement an RPC type semantic between clients by using a messaging Broker..

A-MQ7 Broker
Client
Requester
Client
responder
Work
Queue
Reply
Queue

Message
-----------
ReplyTo
1
2
3
4

A client can make a remote call on another client by sending a message to a work queue (step 1) and defining a reply queue that another client can use to send a response. This reply queue is usually transient and coupled to the client requester but does not have to be.

Another client can consume from the work queue (step 2) and carry out some function or task using information in the message. Once the work has been carried out the work or responder client can send a message to the reply queue usually containing some information on the outcome of the work carried out.

The client requester will then consume the reply message from its reply queue and inspect the message for the outcome.